## Slide 1
Requirement 1 | RC Car Control
Button-driven LED2 status and CAN-based distance detection
START
Initialize CAN1, GPIO, CMT0
Initial: LED1 OFF | LED2 OFF | CarStatus = 0
PUSH BUTTON / LED2 / CARSTATUS
TOGGLE / LED1 / DISTANCE SENSOR
YES
NO
Sample and debounce PK0
20 stable callbacks
Hold >= 10 s?
Button fault active
LED2 blinks continuously
CarStatus = 2
After short release, wait 3 s
and toggle LED2
OFF -> CarStatus 0
ON -> CarStatus 1
Read CAN ID 0x201: MotorDuty + DistanceSensor
Normal detection needs LED2 ON, MotorDuty > 0, toggle ON, no fault
Detection enabled?
Disabled
LED1 OFF
OD = 0
NO
YES
1-10
OD = 3 | Car = 3
LED1 ON
11-100
OD = 2
LED1 ON
101-255
OD = 1
LED1 blinks
Other
OD = 0
LED1 OFF
TOGGLE-OFF EXCEPTION LED2 ON + MotorDuty > 0 + distance 0-10 -> LED1 ON; ObjectDetectionStatus = 0
CANalyzer output | CAN ID 0x102 | Byte 0: CarStatus | Byte 1: ObjectDetectionStatus | Send on change or 20-callback timeout

## Slide 2
01 Startup and Push Button -> LED2
Mapping: initialization, input debounce, delayed short press, and 10-second hold fault.
01 Startup + GPIO
main() sets initial outputs
src/Requirement_1.c | lines 32-46
CAN1Init();
PORT9.PODR.BIT.B5 = 0;
PORT9.PODR.BIT.B6 = 0;
CMT0_init();
02 CAN receive + timer
CAN1Init() / CMT0_init()
src/Requirement_1.c | lines 210-244
R_CAN_RxSet(1U, CAN_RX_MAILBOX, 0x201U, DATA_FRAME);
R_CAN_Control(1, OPERATE_CANMODE);
R_CMT_CreatePeriodic(1000, INT_Excep_CMT0_CMI0, &channel);
03 Debounced press
Short release path
src/Requirement_1.c | lines 98-117
} else if (++debounceTicks >= 20U) {
stableButtonState = rawButtonState;
debounceTicks = 0U;
...
if (stuckButtonFault == 0U) {
releaseDelayTicks = 3000U;
04 Long-hold fault
LED2 blink + CarStatus
src/Requirement_1.c | lines 123-141, 176-177
if (buttonHoldTicks >= 10000U) {
stuckButtonFault = 1U;
if (++led2BlinkTicks >= 500U) {
led2BlinkState = (unsigned char)!led2BlinkState;

## Slide 3
02 CAN Input and Distance Detection
Normal detection requires LED2 ON, MotorDuty > 0, toggle ON, and no stuck-button fault.
05 Read MotorDuty + distance
src/Requirement_1.c | lines 78-82
if (R_CAN_RxPoll(1U, CAN_RX_MAILBOX) == R_CAN_OK) {
if (R_CAN_RxRead(1U, NORMAL_MAILBOX_MODE, CAN_RX_MAILBOX, &rxFrame) == R_CAN_OK) {
motorDuty = rxFrame.data[0];
distanceSensor = (unsigned short)rxFrame.data[1] | ((unsigned short)rxFrame.data[2] << 8);
06 Normal detection gate
src/Requirement_1.c | lines 144-146
detectionEnabled = (unsigned char)((led2State != 0U)
&& (motorDuty > 0U) && (toggleIsOn != 0U)
&& (stuckButtonFault == 0U));
07 Toggle-OFF exception
src/Requirement_1.c | lines 147-150
if ((led2State != 0U) && (motorDuty > 0U)
&& (toggleIsOn == 0U) && (distanceSensor <= 10U)) {
PORT9.PODR.BIT.B5 = 1U;
led1BlinkTicks = 0U;
08 Classify distance range
src/Requirement_1.c | lines 152-170
101-255: objectDetectionStatus = 1U; LED1 blinks
11-100: objectDetectionStatus = 2U; LED1 ON
1-10: objectDetectionStatus = 3U; LED1 ON
other: objectDetectionStatus = 0U; LED1 OFF

## Slide 4
03 CarStatus and CANalyzer Output
CAN ID 0x102 | DLC 8 | Byte 0: CarStatus | Byte 1: ObjectDetectionStatus
09 Select CarStatus
Fault first, then close range
src/Requirement_1.c | lines 174-181
if (faultActive != 0U) {
carStatus = 2U;
} else if ((detectionEnabled != 0U)
&& (distanceSensor >= 1U) && (distanceSensor <= 10U)) {
carStatus = 3U;
} else { carStatus = (led2State != 0U) ? 1U : 0U; }
10 Build + send CANalyzer
status frame
src/Requirement_1.c | lines 184-195
txFrame.id = 0x102U;
txFrame.dlc = 8U;
txFrame.data[0] = carStatus;
txFrame.data[1] = objectDetectionStatus;
(void)R_CAN_TxSet(1U, NORMAL_MAILBOX_MODE, CAN_TX_MAILBOX, &txFrame, DATA_FRAME);